## Slide 1: The Angstrom Project: The Angstrom Project: Building 1000-Core Computer Systems Anant Agarwal CSAIL, MIT

## Slide 2
Stata Center
MIT’s largest laboratory with ~1000 members
Architecture & Programming:
Manycore architectures
Organic or self-aware computing
Languages for scalable computing
Reconfigurable HW, Rapid Prototyping
Provably Reliable Software
Program analysis
Theory:
Theory of distributed systems
Cryptography & Information Security
Mechanism Design
Quantum Information Science
Computational Biology
Human/Computer Interactions:
Spoken language systems
Graphics, Vision, Image processing
Natural language understanding
Gesture-based interfaces
Web automation
Crowd sourcing
AI & Robotics:
Intelligence Initiative
Medical decision making
Machine Learning
Autonomous vehicles
Robot locomotion & control
Systems:
Parallel and distributed systems
Wireless protocols and coding
Mobile and mesh networks
Relational databases
Security & recovery
Medical Telepresence
Mesh
Router
Compute
Core
Cache
eDRAM
PEP core
WDM
Hub

## Slide 3
Project Angstrom:
Building 1000-Core Processor Systems
emesh
Router
Compute
Core
Cache
eDRAM
Partner
WDM
Hub
SEEC Architecture API
Energy
Locality
Perf. Events
HW-Config
Security-Level
OS
Self Aware Factored OS – SEFOS
Observe
Decide
Act
Runtimes
Compiler
Smart Locks
ZetaBricks
Autotuning
Compiler
Peta-
Bricks
Heartbeats and Adaptive Tuners
Partner Core Software
SEEC Application API
Goals
Energy-Budget
Heartrate
Constraints
Security-Level
Prog. Model
Goals
Sketches
Applications
Streaming Sensor
Chess
Dynamic Graph
HPC
Algorithmic Choice
Observe
Decide
Act
Learner
Perf. Models
Heartbeats
Goals met?
Cntrl Sys
Notes: 3
3
3

## Slide 4: Challenges to Exascale Computing: The 3 P’s
Easy to get two of three, hard to get all three
Performance
Power Efficiency
Programmability
Performance
Power Efficiency
Programmability
Performance
Power Efficiency
Programmability
Performance
Power Efficiency
Programmability

## Slide 5: “Flopping ALUs” are Energy Efficient
But are about as programmable as a paperweight
Big FLOPS
Low Energy

## Slide 6: How to Get All Three
Performance and scalability
Power Efficiency
Programmability
1. Fully distributed tiled architecture
2. SEEC technology

## Slide 7
Broadcast
network using WDM optical
Electrical
express
mesh
network
1000 cores
5TFLOPS 1.5GHz
50W (50mW/tile)
Core:
32KB L1i
64KB L1D
256KB L2
1MB eDRAM
Mesh
Router
Compute
Core
Cache
eDRAM
PEP core
WDM
Hub
Ultra-low power SRAM cell
Distribute everything so things are close by
No large central structures
Fully Factored Angstrom Chip Design – Yields Energy Efficiency and Scalability

## Slide 8: What Core to Use
You don’t
10W/core to 50mW per core!
Start with embedded tile core
Go from 300mW to 50mW

## Slide 9: Tiled Approach is Power Efficient and Scalable
PCIe 1
MAC
PHY
PCIe 0
MAC
PHY
Serdes
Serdes
Flexible IO
GbE 0
GbE 1
Flexible IO
UART, HPI
JTAG, I2C,
SPI
DDR2 Memory Controller 3
DDR2 Memory Controller 0
DDR2 Memory Controller 2
DDR2 Memory Controller 1
XAUI
MAC
PHY 0
Serdes
XAUI
MAC
PHY 1
Serdes
PROCESSOR
P2
Reg File
P1
P0
CACHE
L2 CACHE
L1I
L1D
ITLB
DTLB
2D DMA
STN
MDN
TDN
UDN
IDN
SWITCH
Example: TilePro64
200Gbps memory BW
40Gbps I/O
150GOPS
20W

## Slide 10: 2. SEEC: A New Computational Model
Self-Aware Execution (SEEC) – a computing paradigm in which systems observe their runtime behavior, learn, and take actions to meet desired goals
User indicates performance or energy goals and provides alternatives of how to do things
System hardware and software manage everything else (e.g., locality, resilience), meeting goals by adapting to changing conditions
Observe
Decide
Act
Learner
Perf. Models
Heartbeats
Goals met?
Cntrl Sys

## Slide 11: 2. SEEC – Self Aware Computational Model
Factored
Operating
System
Disk
DRAM
App 2
App 1
App 3
voltage, freq
Memory
Manager
File
System
Scheduler
power, temp
App 1
Analysis &
Optimization
Engine
Observe
Decide
Act
Core
Cache
App 2
App 3
Learner
Core
Cache
goals
Perf. Models
www.youtube.com/user/HeartbeatsAPI
heartrate
Heartrate lower than user goal
Power is manageable
Increase core frequency
Computers should become more like humans
Partner core
Cache
Partner core
Cache
Partner core
Cache
Notes: 11

## Slide 12: Why SEEC? Programming is Becoming very Hard
  Mini-SAR app has many configurations in existing or future machines
    # threads/stage
    Thread mapping  cores
    Core frequencies and voltage
    Memory controller mapping
    Layout of threads and cores
    Cache management
    What if something breaks – I lose a core!
  Measured range of 0.07 - 0.7 pulses/sec/watt for various configurations (10X range) – 10X in energy efficiency on the table!
    Programmer can easily make bad choices in configuration
    Best configuration can also change with input
    Communication and cache variability
12
SEEC technology achieved 90% of optimal with minimal programmer effort
mini-SAR frontend

## Slide 13: Roles in the SEEC Model
 | Application Developer | Systems Developer | SEEC System Infrastructure
 | Express application goals and progress (e.g. frames/ second) |  | Read goals and performance
 |  |  | Determine how to adapt (e.g. How to speed up the application)
 |  | Provide a set of actions and a callback function (e.g. allocation of cores to process) | Initiate actions based on results of decision phase
13
Observe
Act
Decide
The decision engine is key to enabling SEEC
13
Notes: 13

## Slide 14: ODA Control Loop
Act
Observe
Decide
Cores
Power
Memory
System Parameters
Heartbeats API
A control theory for Sefos
Control system
Learning engine
Heuristic models
User can dial in desired behavior
14
Notes: 14
14

## Slide 15: H.264 Video Encode: Procedural
15
Open Movie file

## Slide 16: H.264 Video Encode: Self-Aware using Heartbeats plus Heuristic Approach
16
Open Movie file

## Slide 17: Minimizing Power in a Self-Aware System
0
10
20
30
40
50
60
70
80
50
150
250
350
450
Time (Heartbeat)
Performance (Frame/s)
130
140
150
160
170
180
0
2
4
6
8
10
12
14
16
Time (s)
Power (W)
Performance
Power
Performance goal
Notes: 17

## Slide 18: Multiple Applications
bodytrack
x264
Clock drops 2.4-1.6GHz
w/o SEEC app misses goals
SEEC allocates cores to bodytrack
w/o SEEC app exceeds goals
SEEC removes cores from x264
SEEC adjusts algorithm to meet goals
18
Notes: 18

## Slide 19: Decision Making Strategies
19

## Slide 20: Decision Making Strategies Comparison of Different Approaches
20
*(lower is better)
WDP: measures the percentage of data points that are not in the desired performance interval

## Slide 21: Summary
  Angstrom project is approaching the computing problem with two key ideas
    Create a fully distributed architecture
    Create a fundamentally new computational model – SEEC
  Angstrom approach has the potential to solve the power efficiency, performance and programmability challenges
  SEEC approach is showing promise as a new way of building computer ystems
21