## Slide 1: VSIPL and SAR Performance on Multiple Generations of Intel® Processors
Peter Carlston,
Platform Architect,
Embedded Computing Division
Intel Corporation

## Slide 2: VSIPL and SAR Benchmark Systems
Benchmark Systems and Methodology
  Freescale MCP8641D (2007) @ 1 GHz
    GE Fanuc DSP230 single board computer; AXISLib VSIPL 2.3; VxWorks 6.6; 2 cores; 1MB cache/core; ~25W max processor power
  Intel Core 2 Duo SL9400 (2008) @ 1.86 GHz
    HP 2530P Laptop; N.A. Software VSIPL Beta for Intel Architecture; Linux; 2 cores; 6 MB shared cache; 31.5 W max power incl. chipset
  Intel Core i5-430M (2010) @ 2.0 GHz (fixed)
    Acer Aspire AS5741-6823 Laptop; N.A. Software VSIPL AVX Beta; Linux; 2 cores; 3MB shared cache; ~39W max power incl. chipset
  Intel Core i7 2710QE (2011) @ 2.0 GHz (fixed)
    Intel ‘Emerald Lake’ Customer Ref. Board; N.A. Software VSIPL AVX Beta; 4 cores; 6MB shared cache; Linux; ~51W max power incl. chipset
  Intel Core i7-2715QE (2011) @ 2.1 GHz; Intel Turbo Boost enabled
    GE Intelligent Platforms DSP280; AXISLib-AVX Beta; 1.0; Scientific Linux 6.0 x64, Kernel 2.6.32; ~51W max power incl. chipset
VSIPL Tests conducted by GE-IP and NA Software 2009-2011
  Single Thread tests only; data in warm caches where possible
SAR/SARMTI Tests conducted by NA Software, 2010

## Slide 3: VSIPL 1D FFT Relative Performance
Chart: 1D c-c FFT MFLOPS
| 256 | 1K | 4K | 16K | 256K | 512K
Freescale* MPC8641D | 4266.6667 | 5120 | 3442.0168 | 2770.2415 | 1026.2271 | 673.0906
Intel® Core™ 2 Duo SL9400 | 8126.9841 | 8126.9841 | 6845.6825 | 5821.7259 | 5015.5102 | 4245.4279
Intel® Core™ i5-430M IPP SSE | 8258.0645 | 9516.7286 | 7646.5464 | 9852.921 | 3965.2034 | 3747.7321
Intel® Core™ i7-2710QE NAS AVX | 23272.7273 | 28131.8681 | 18788.9908 | 13572.5444 | 14246.9565 | 9963.4647
Intel® Core™ i7-2715QE DSP280 AVX | 20078.4314 | 36571.4286 | 29934.2266 | 23127.2434 | 18547.9245 | 8430.4942
2008 Intel processor vs Freescale: Clock speed benefits Intel <256K points; 6M L2 cache benefits Intel > 256K points
2010 Intel processor: Minor or no improvement vs 2008 Intel processor
2011 Intel processor: Major micro-architecture enhancement: 2x load/store bandwidth; ring bus; 256-bit SIMD registers (Intel® AVX)
vsip_ccfftip_f

## Slide 4: VSIPL and SAR Performance on Multiple Generations of Intel® Processors
VSIPL* Function | Intel® Core™ Processor 2011 vs Freescale* MPC-8641D | Intel® Core™ Processors 2010 vs 2008 | Intel® Core™ Processors 2011 vs 2008 | Intel® Core™ Processors 2011 vs 2010 | Intel® Core™ i7- 2011 AVX vs SSE
1D FFT | 5 – 14 X | < 1.1X | 2.4 - 3.5 X | 2.3 – 3.5 X | 1.2 - 1.8 X
Multiple 1D FFT | 5.4 – 10.4 X |  | 2.5 – 3.3 X | 2.6 – 3.7 X | 1.3 – 1.6X
2D FFT, non-square matrices | No Data |  |  | 2 – 2.3 X | 0.7 – 1.3X
2D FFT, smaller square matrices |  |  |  | 2.3 – 3.1 X | 1.1 – 1.6 X
Complex Matrix Transpose | 7 – 26 X | < 1.1X | 0.6 – 2.14 X | 2 – 4.1 X | None
Vector Multiply | 4.6 – 72 X |  | 2.3 – 8.3 X | 2.1 – 4.5 X | 1 – 2.9 X
Vector Sine | 1.1 – 1.4 X |  | 3.6 – 3.7 X | 3.1 – 4.7 X | 0.4 – 1.8 X
Vector Cosine | 1.1 – 1.4 X |  | 2.2 – 2.6 X | 2.8 – 2.9 X | 1.4 X
Vector Square Root | 2.6 – 4.5 X |  | 2.3 – 3.2 X | 2.3 – 2.9 X | 1.2 -2.1 X
Vector Scatter | No Data |  |  | 4.2 – 8.2x | 1.5 – 4.1 X
Vector Gather |  |  |  | 2.5 – 4.8x | 1.5 – 4.1 X

## Slide 5: SAR/SARMTI Performance on 2010 and 2011 Intel® Processors
  Core for core, the 2011 Intel® processor performs >2X better on these algorithms
  Running with 4 threads yields a 3-4X performance benefit (additional 12W max thermal design power)
N.A. Software Algorithm | System | 2 Threads (cores) | 4 Threads (cores)
SAR | Intel® Core™ i7-2710QE with Intel® AVX 1.0 (2011) | 0.059 s | 0.027 s
 | Intel® Core™ i5-430M with Intel SSE 4.2 (2010) | 0.135 s | 0.121 s*
 | Intel® Core™ i7-2710QE Speed Up | 2.3X | 4.4X
SARMTI | Intel® Core™ i7-2710QE with Intel® AVX 1.0 (2011) | 6.03 s | 3.841 s
 | Intel® Core™ i5-430M with Intel SSE 4.2 (2010) | 15.197 s | 13.667 s*
 | Intel® Core™ i7-2710QE Speed Up | 2.5X | 3.5X
* 4 thread timings utilize Intel Hyper Threading since only a 2-core version is available.