## Slide 1: Accelerating Bit Error Rate Simulation in MATLAB using Graphics Processors
1
© 2011 The MathWorks, Inc.
James Lebak
Brian Fanous
Nick Moore
High-Performance Embedded Computing Workshop (HPEC 2011)
22 September 2011

## Slide 2: Outline
Application Area
MATLAB Tools
DVB-S.2 Subset benchmark
DVB-S Subset benchmark
Conclusions

## Slide 3: Bit Error Rate Simulation
Begin with a model of a communications system
Vary the signal-to-noise ratio
Calculate bit error rate through Monte Carlo simulation
Obtain a curve like that at the right
Expensive (millions of trials, days of simulation)

## Slide 4: Example System Model Digital Video Broadcast Standard, Second Generation (DVB-S.2)
BCH
Encoder
Demodulator
and Deinterleaver
LDPC
Decoder
LDPC
Encoder
BCH
Decoder
Channel
Model
Modulator
and
Interleaver
Data In
Data Out
Transmitter Model
Receiver Model
LDPC = Low-Density Parity Check
Simulation Goal: Verify transmitter and receiver achieve a given bit error rate in the presence of noise introduced by the channel model
Notes: Red boxes have been ported to be GPU System objects.
DVB-S.2 (Digital Video Broadcasting, 2nd generation). Used by Dish Networks, etc.

## Slide 5: Outline
Application Area
MATLAB Tools
DVB-S.2 Subset benchmark
DVB-S Subset benchmark
Conclusions

## Slide 6: System Objects
  Represent dynamic systems
  Algorithms with input values and states that change over time
  Optimized for iterative execution
    One-time checking of parameter values, input arguments
    Data streaming between objects
  Many algorithms implemented in C++ for speed
  Support for automatic C code generation
  System objects allow design of dynamic systems in MATLAB
Notes: System objects extend MATLAB to represent dynamic systems. I’ve mentioned “dynamic systems” a number of times now – these are algorithms with input values and internal states that change over time. Such systems typically require more than a simple “y equals function of x” computation. They typically have one-time initialization code, repetitive calls to output computations, periodic reset tasks, and termination code, to name a few. They update and maintain internal states of the System over time. System objects define and encapsulate all these tasks and states within its model of a dynamic system.
(click) This task decomposition leads to one reason System objects are highly efficient for iterative execution or processing streaming data in MATLAB: parameter values and input arguments are validated once, during the first iteration of the object. After that, these time-consuming validation and error-checks are replaced by simpler, more efficient internal checks as needed during subsequent loop iterations. We’re finding faster execution in many systems. Also, System objects support automatic code generation, so C-code execution performance is always available. We’ll talk more about code generation later in this presentation.
(click) They help overcome system complexity by providing a common interface for implementing these algorithms, regardless of the algorithm you choose. Once you’ve learned how to work with one System object, you’ve learned how to work with every System object.
(click) System objects can be used in both MATLAB and Simulink. “MATLAB teams” and “Simulink teams” can share the same algorithm and leverage each other’s work. For example, you are able to develop algorithms in MATLAB and re-use them in Simulink when your project requirements demand Simulink features such as hybrid system simulation, physical modeling, and graphical block diagrams.

## Slide 7: System Object Receiver Model
%***Receiver Object Creation ***
hDemod = comm.PSKDemodulator(demodulatorArgs{:});
hDeintrlv = comm.BlockDeinterleaver(dvb.InterleaveOrder);
hDec = comm.LDPCDecoder(decoderArgs{:});
{'ModulationOrder', 2^dvb.BitsPerSymbol, ...
'BitOutput', true, ...
'PhaseOffset', dvb.PhaseOffset, ...
'SymbolMapping', 'Custom', ...
'CustomSymbolMapping', dvb.SymbolMapping, ...
'DecisionMethod', 'Approximate log-likelihood ratio', ...
'Variance', dvb.NoiseVar}
%***Receiver Model Execution***%
demodOut = step(hDemod, chanOut);
dexlvrOut = step(hDeintrlv, demodOut);
ldpcdecOut = step(hDec, dexlvrOut);

## Slide 8: Graphics Processing Unit (GPU) Acceleration in MATLAB
Requirements
  Parallel Computing Toolbox
  NVIDIA GPU with Compute Capability 1.3 or greater
Level of control
Minimal
Some
Extensive
Use GPU arrays with MATLAB built-in functions
Execute custom functions on elements of GPU arrays
Create kernels from existing CUDA code and PTX files
Parallel options
Required effort
None
Straightforward
Involved

## Slide 9: LDPC Decoder
c0
c1
c2
c3
c4
c5
c6
c7
c8
f0
f1
f2
f3
f4
c9
fj
ci
rji
qij
LDPC Decoder Algorithm
for ii=1:maxIterations,
Update all r messages (in parallel)
Update all q messages (in parallel)
end
form hard/soft decision (in parallel)
LDPC Decoder was implemented using custom CUDA kernels in MATLAB release R2011a
Received word
Check nodes
Iteratively determine message bits that best satisfy system constraints
(64800 nodes)
(32400 nodes)
~226,000 edges
Notes: rji is Log of ratio fj check is satisfied, given received bit i is 0/1 give info not from ci
Qij is Log of ratio Pr(ci = 1/0| received bit & info not from fj)

## Slide 10: GPU-Accelerated Receiver Model
%***Receiver Object Creation ***
hDemod = comm.PSKDemodulator(demodulatorArgs{:});
hDeintrlv = comm.BlockDeinterleaver(dvb.InterleaveOrder);
hDec = comm.gpu.LDPCDecoder(decoderArgs{:});
%***Receiver Model Execution***%
demodOut = step(hDemod, chanOut);
dexlvrOut = step(hDeintrlv, demodOut);
ldpcdecOut = step(hDec, dexlvrOut);
Minimal code changes to use GPU System Object
GPU System object is 20x faster than original System object
Overall system simulation is 5x faster

## Slide 11: Outline
Application Area
MATLAB Tools
DVB-S.2 Subset benchmark
DVB-S Subset benchmark
Conclusions

## Slide 12: DVB-S.2 Subset Benchmark Digital Video Broadcast Standard, Second Generation (DVB-S.2)
BCH
Encoder
Demodulator
and Deinterleaver
LDPC
Decoder
LDPC
Encoder
BCH
Decoder
Channel
Model
Modulator
and
Interleaver
Data In
Data Out
Transmitter Model
Receiver Model
Subset benchmark (can execute entirely on GPU)
New objects implemented using MATLAB for faster development
Notes: Red boxes have been ported to be GPU System objects.
DVB-S.2 (Digital Video Broadcasting, 2nd generation). Used by Dish Networks, etc.

## Slide 13: Using GPU System objects
GPU System objects are drop-in replacements for standard System objects
  Normal MATLAB arrays in  normal MATLAB arrays out
  Requires two data transfers
%***Receiver Object Creation ***
hDemod = comm.gpu.PSKDemodulator(demodulatorArgs{:});
hDeintrlv = comm.gpu.BlockDeinterleaver(dvb.InterleaveOrder);
hDec = comm.gpu.LDPCDecoder(decoderArgs{:});
%***Receiver Model Execution***%
demodOut = step(hDemod, chanOut);
dexlvrOut = step(hDeintrlv, demodOut);
ldpcdecOut = step(hDec, dexlvrOut);

## Slide 14: Using GPU System objects
GPU System objects are drop-in replacements for standard System objects
  Normal MATLAB arrays in  normal MATLAB arrays out
  Requires two data transfers
GPU System objects also accept GPUArrays as inputs
  In this case the output is also a GPU Array
  Avoids data transfer overhead
%***Receiver Object Creation ***
hDemod = comm.gpu.PSKDemodulator(demodulatorArgs{:});
hDeintrlv = comm.gpu.BlockDeinterleaver(dvb.InterleaveOrder);
hDec = comm.gpu.LDPCDecoder(decoderArgs{:});
%***Receiver Model Execution***%
demodOut = step(hDemod, gpuArray(chanOut));
dexlvrOut = step(hDeintrlv, demodOut);
ldpcdecOut = gather(step(hDec, dexlvrOut));

## Slide 15: DVB-S.2 Subset Benchmarks Using GPUArray
Chart: Speedup Over CPU
| CPU Input | GPUArray input
GPU-Accelerated LDPC | 14.3678 | 15.2439
All GPU-Accelerated | 12.1714 | 13.4409
Baseline: speed of subset with all objects on the CPU
Using GPUArray objects as inputs accelerates both versions of the benchmark
Using the GPU-accelerated LDPC provides a large performance boost
Adding GPU-accelerated versions of other objects slows down the simulation
Benchmark Machine Specs
  CPU: 2.5 GHz Intel Core 2 Quad
  GPU: NVIDIA Tesla C1060
  Windows 7
  MATLAB R2011b

## Slide 16: Performance vs. Input Size for GPU System Objects
Computational density is important for obtaining good GPU performance
Many GPU System objects are slower for small data sizes
In R2011b, crossover point is generally around 105
Frame size is 64800 elements
System Frame Size

## Slide 17: DVB-S.2 Subset Multi-Frame Benchmarks
Chart: Speedup Over CPU
| CPU Input | GPUArray input | GPUArray, 8 frames per step
GPU-Accelerated LDPC | 14.3678 | 15.2439 | 15.2439
All GPU-Accelerated | 12.1714 | 13.4409 | 17.1233
Process 8 frames of data on the GPU simultaneously to get better performance
LDPC performance begins to saturate, but other objects become faster

## Slide 18: Outline
Application Area
MATLAB Tools
DVB-S.2 Subset benchmark
DVB-S Subset benchmark
Conclusions

## Slide 19: Digital Video Broadcast – Satellite (DVB-S) benchmark
Demodulator
Viterbi
Decoder
Convolutional
Encoder
Channel
Model
Modulator
Data In
Data Out
Transmitter Model
Receiver Model
DVB-S is a similar system
  uses different encoder/decoder pair than DVB-S.2
The entire chain executes on the GPU
  including message generation and validation
Viterbi Decoder is implemented as a custom CUDA kernel
  all others implemented using MATLAB GPU support

## Slide 20: DVB-S Subset Benchmarks
Chart: Mean execution time per frame (s)
| CPU Input
CPU | 0.0064
GPU Viterbi | 0.0037
GPU All, single-frame | 0.0193
GPU All, 500 frames | 0.0004143
Generated CPU code | 0.0036
DVB-S frame size is 1632 elements
  single-frame performance on the GPU is slower than the CPU
  multi-frame performance is much faster

## Slide 21: Conclusions
The GPU can be a powerful tool for accelerating Bit Error Rate simulation in MATLAB
Parallel Computing Toolbox allows a trade-off between work and performance
  Implement the kernels with highest computational requirements as custom CUDA kernels
  Implement kernels with lower computational requirements using MATLAB
For best performance using the GPU, process multiple data frames simultaneously

## Slide 22: Acknowledgments
The following people at MathWorks contributed to this work or to the presentation.
Andy Grace
Witek Jachimczyk
Amit Kansal
Darel Linebarger
Mike Longfritz
Roy Lurie
Mike McLernon
Don Orofino
Paul Pacheco
Narfi Stefansson
Bharath Venkataraman