## Slide 1: Hardware Based Floating Point Processing
All the ingredients for FPGA based floating point
  28 nm Variable Precision DSP Block
    28nm silicon enhancements for floating point
  IP: Fused Datapath: efficient floating point in Altera FPGAs
  Tools: DSP Builder Advanced Blockset
    Matlab/Simulink native support is floating point
Cholesky decomposition / matrix inversion design
  Programmable in both matrix size and vector size
    Ex: 20x20 with vector size of 10, 240x240 with vector size of 60
  Up to 1 Million matrices per second in a single core for time interleaved 20x20 matrices, multiple cores possible in single device
Floating point roadmap
  Silicon / Tools / IP

## Slide 2: Single Channel Results: Single Core
Single Channel Cholesky Inversion Core |  |  |  | 
Matrix Size | Vector Size | Dot Product Utilization | Throughput (matrices/sec) | Latency (us)
240x240 | 60 | 90.1% | 3282 | 489
200x200 | 50 | 88.3% | 4619 | 349
100x100 | 50 | 57.4% | 17,700 | 97.8
75x75 | 50 | 40.7% | 24,900 | 66.7
50x50 | 50 | 24.8% | 37,400 | 41.3
100x100 | 25 | 70.3% | 14,400 | 110.8
75x75 | 25 | 52.5% | 22,800 | 70.2
50x50 | 25 | 31.2% | 37,200 | 41.5
25x25 | 25 | 12.9% | 73,800 | 19.4
Multiple single precision Cholesky cores may be implemented within a single FPGA |  |  |  | 

## Slide 3: Multi-channel Results: Single Core
Multi-Channel Cholesky Inversion Core |  |  |  |  | 
Matrix Size | Vector Size | Number of channels | Dot Product Utilization | Throughput (matrices/sec) | Latency (us)
100x100 | 50 | 6 | 96.8% | 29,900 | 380
50x50 | 50 | 20 | 98.3% | 148,000 | 270
75x75 | 25 | 10 | 98.3% | 42,700 | 392
50x50 | 25 | 20 | 98.7% | 118,000 | 304
25x25 | 25 | 20 | 95.6% | 526,000 | 71
20x20 | 20 | 50 | 97.8% | 1,000,000 | 96
Multiple single precision Cholesky cores may be implemented within a single FPGA |  |  |  |  | 

## Slide 4: Cholesky Throughput per FPGA device
Cholesky Throughput per Stratix V FPGA |  |  |  |  | 
Matrix Size | Vector Size | Device: Stratix V 5SGSD8 | Number of cores per FPGA | Throughput per core (matrices/sec) | Throughput per FPGA device (matrices/sec)
20x20 | 20 | single die, 700 kLE, 4000 mults | 18 | 1M | 18 Million
240x240 | 60 |  | 6 | 3,000 | 18 Thousand
Multiple Cholesky cores implemented within a single FPGA |  |  |  |  |