## Slide 1: Optical Interconnects for Computing Applications
Mitchell Fields, Ph. D. mitch.h.fields@avagotech.com

## Slide 2: Evolution of high-bandwidth interconnects
Throughout history, optical interconnects were adopted when they overcame limitations of electrical signaling:
Distance / Bandwidth / Density / Power
For optical interconnects in computing environments, COST and POWER are the most critical metrics.
Computing

## Slide 3: Modules targeted at different design points
Platform | AFBR-75 | MicroPOD
Application range | Consumer and low-BW computer interconnects | HPC and high-BW system interconnects
Aggregate bandwidth | 20G | 120G
IC technology | CMOS | BiCMOS
Laser source | 2xVCSEL array | 12xVCSEL array
Receiver | 2xPiN array | 12xPiN array
Electrical socket | Socket | mLGA
Optical connector | J-cable | Prizm
Footprint (with and w/o socket and optical connector) | 12x12x2 16x16x2.3 | 7.8x8.2x3.9 10.7x11.1x7.1
Power (mW/Gbps) | 14 | 25
Nominal reach (m) | 30 | 100
Diagnostic capability | ID and basic alarms | Full diagnostics
Signal integrity features | None | Equalization and de-emphasis

## Slide 4: MicroPOD: Driven by high-performance computing
MicroPOD: 8.2mmx7.8mm 12-channel 10G Tx and Rx modules
IBM Hub Module: 28 Tx/Rx MicroPOD pairs (~6 Tbps I/O!)
IBM Power775 drawer: 8 Hub modules
IBM Power775 Datacenter in a rack: 12 drawers / ~100TF
HPC Challenge: Unprecedented sustained computing power
Partnership for differentiation
To build the world’s most powerful computing system, IBM required a novel optical interconnect. MicroPOD was designed for low cost and high performance.

## Slide 5: AFBR-75 Optical Module detailed overview
Electrical
12mm x 12mm
IC
2 Photo-detectors
2 Lasers
Alignment hole
Avago
Optical Transceiver IC
Module Lens
Module PCB
Tx1
Tx2
Rx1
Rx2
Optical
Optics for the consumer market utilized for computer networking.