## Slide 1: Data Flow Compilation for Greater Parallelism
Does not require new languages or ‘parallel programming’, only ‘restrict’ keyword for memory separation
Replace traditional sequential compilation with DataFlow compilation
Remove core specific L1 cache for ‘shared’ data
Allow non-memory based core-to-core communication
 | Intel Core i7-965 (3.2GHz) | Dual Intel Xeon E5620 (2.4GHz) | Dual AMD Opteron 6134 (2.3GHz)
gcc –m32 –O2 | 0.0359 GUPS | 0.0291 | 0.0127
CHiMPS, 2 core | 0.0648 (1.8x) | 0.0493 (1.7x) | 0.0150 (1.2x)
CHiMPS, 4-core | 0.0886 (2.5x) | 0.0664 (2.3x) | 0.0206 (1.6x)
GUPS (random memory access) results
 | Intel Core i7-965 (3.2GHz) | Dual Intel Xeon E5620 (2.4GHz) | Dual AMD Opteron 6134 (2.3GHz)
gcc –m32 –O2 | 71 seconds | 85 seconds | 249 seconds
CHiMPS, 2 core | 62 seconds (1.14x) | 87 seconds (0.97x) | 181 seconds (1.3x)
CHiMPS, 4-core | 40 seconds (1.7x) | 68 seconds (1.25x) | 163 seconds (1.5x)
DGEMM (sequential memory access) results
Results from compilation item only with traditional architectures
Other items require new silicon
 | Intel Core i7-965 (3.2GHz) | Dual Intel Xeon E5620 (2.4GHz) | Dual AMD Opteron 6134 (2.3GHz)
gcc –m32 –O2 | 6.6 seconds | 6.6 seconds | 13 seconds
CHiMPS, 2 core | 2.9 seconds (2.27x) | 3.8 seconds (1.73x) | 7.7 seconds (1.68x)
CHiMPS, 4-core | 2.3 seconds (2.86x) | 2.7 seconds (2.44x) | 7.0 seconds (1.85x)
Discrete (Finite Differential Solver) results

## Slide 2: Replace traditional sequential compilation with DataFlow compilation
Source code
Traditional compilation
v = w+z
s = v+2
t = u+y;
q = t+s;
return q
u = x+y;
DataFlow compilation
long f(long w, long x,
long y, long z)
{
long u = x+y;
long v = w+z;
long s = v+2;
long t = u+y;
long q = t+s;
return q;
}
Enter function f
…
Allow each instruction or group of instructions to execute on a separate core (yellow and orange)
Requires core-to-core communication for partial results
Dataflow graph allows optimizations that are not apparent in traditional control flow graph (e.g. memory parallelism)
Far more parallelism can be extracted than possible by human intervention
Add_1
Add_2
z
w
x
y
Add_4
u
2
Add_3
v
Add_5
Enter f
t
s
Exit f
t

## Slide 3: Remove core specific L1 cache for ‘shared’ data
Shared data : at least one core has write access and another core has read and/or write access
L2 CCC cache: Crossbar connected cache with banking for better multicore access
CPU Core
L1
Inst Cache
Shared L2 Cache
L1 Data Cache
CPU Core
L1
Inst Cache
L1 Data Cache
Traditional architecture
(cache coherency issues for shared data)
CPU Core
L1
Inst Cache
Shared CCC L2 Cache
L1 Data Cache
CPU Core
L1
Inst Cache
L1 Data Cache
Modified architecture: L1 cache not used for shared data
(no cache coherency issues)
Shared data
Shared data

## Slide 4: Allow non-memory based core-to-core communication
Partial results computed in one core, passed to another core directly.
Does not affect (fill) caches.
Temporary data that never lives in ‘off-chip’ memory.
CPU Core
L1
Inst Cache
Shared L2 Cache
L1 Data Cache
CPU Core
L1
Inst Cache
L1 Data Cache
Traditional architecture
(core-to-core data transfer goes through L1/L2 cache as shared data)
CPU Core
L1
Inst Cache
Shared CCC L2 Cache
L1 Data Cache
CPU Core
L1
Inst Cache
L1 Data Cache
Direct core-to-core communication
(used for partial results which need never live in memory)
Shared data
Shared data
Partial results