## Slide 1: The TILE-Gx Processor: Enabling HPC through Massive-Scale Manycore
Bob Doud
Director of Processor Strategy, Tilera Corp.
HPEC, September 2011

## Slide 2: Tilera TILE-Gx Family
Manycore Processors with up to 100 Cores
Performance
Power Efficiency
I/O & Connectivity
450 BOPS on a single TILE-Gx processor
60 Watts typical power dissipation
>160G of I/O on the processor
5x Performance-per-Watt of x86 class CPUs
Shared, coherent cache across all cores
Integrated quad DDR3 memory controllers
© 2011 Tilera Corporation

## Slide 3: The TILE-Gx8100™ Processor:
System-on-a-Chip with 100 64-bit cores
3
© 2011 Tilera Corporation
Memory Controller (DDR3)
Memory Controller (DDR3)
Memory Controller (DDR3)
Memory Controller (DDR3)
mPIPE
USB x2,
UART x2,
JTAG, I2C,
SPI, GPIO
SerDes
PCIe 2.0
8-lane
SerDes
PCIe 2.0
8-lane
Interlaken
Interlaken
10 GbE
XAUI
SerDes
4x GbE
SGMII
10 GbE
XAUI
SerDes
4x GbE
SGMII
10 GbE
XAUI
SerDes
4x GbE
SGMII
10 GbE
XAUI
SerDes
4x GbE
SGMII
10 GbE
XAUI
SerDes
4x GbE
SGMII
10 GbE
XAUI
SerDes
4x GbE
SGMII
10 GbE
XAUI
SerDes
4x GbE
SGMII
10 GbE
XAUI
SerDes
4x GbE
SGMII
SerDes
PCIe 2.0
8-lane
MiCA
MiCA
450 BOPS
32MBytes
Coherent
Cache
~60 Watts
Runs SMP
Linux

## Slide 4: Peta-Op Integer Compute at <500KW
TILE-Gx100 Processor:
  3-way core, 1.5GHz, 100 cores = 450 BOPS per chip
1 Tilera Server Shelf:
  3U rack space; 12 blades, 3 processors/blade
1 Tilera Rack;
  13 Shelves, 468 processors, 46,800 cores
5 Tilera Racks;
  2250 processors, 225,000 cores; ~450 Kilowatts
© 2011 Tilera Corporation
5 Racks
2250 Tile Processors = 1.012 Peta-Ops
Up to 180 Tbps of I/O
288 TBytes DDR3 Memory
3600 cores

## Slide 5: TILE-Gx Enables a Range of HPC Applications
© 2011 Tilera Corporation
Real-Time Informatics
Cyber Security Data Harvesting
Threat Analysis / Forensics
Video Surveillance & Analysis
Image compression/decompression
Network Security Processing
Intrusion Prevention (IPS/IDS)
Data Leakage Protection (DLP)
Integer Compute
Hyper-Scale Integer Computing
Compute-Intensive SIMD & DSP
Target Tracking / Pattern Recognition

## Slide 6: Thank You
Please stop by our table outside the auditorium
TILE-Gx processor solutions on display
We’ll be happy to discuss your HPC requirements
© 2011 Tilera Corporation